ECGR4161 – Introduction to Robotics
Lab Assignment #3
Shengkai Xu
02-26-2021

Objective:
In this lab student are instructed to make robot to run 1 meter square using motor encoder.

URL of the video:
https://youtu.be/Na4BIT_Mrjs

Commentary:
There was many incorrect reading value when I connected the ultrasonic sensor directly to the micro controller board. Because of the voltage requirement and supply different between the board and ultrasonic sensor, the logic level converter was need to convert the logic value. Using logic level converter it eliminated the voltage fluctuation causing the error reading.

Code Snippet:

#undef min
#undef max
#include <algorithm>

const int trigPin = 32; //This is Port Pin 3.5 on the MSP432 Launchpad
const int echoPin = 33; //This is Port Pin 5.1 on the MSP432 Launchpad

constexpr size_t SAMPLE_IDX = 5;

void setup() {
  pinMode(trigPin, OUTPUT);
  pinMode(echoPin, INPUT);

  Serial.begin(9600);
  Serial.println("HC-SR04 Testing...");
}

long get_sonar_val() {
  long samples[SAMPLE_IDX];
  long centimeters;

  for (int i = 0; i < SAMPLE_IDX; ++i) {
    digitalWrite(trigPin, LOW);
    delayMicroseconds(5);
    digitalWrite(trigPin, HIGH);
    delayMicroseconds(10);

    samples[i] = pulseIn(echoPin, HIGH);

    centimeters = samples[i] / 58;

    Serial.print("Distance = ");
    Serial.print(" ");
    Serial.print(centimeters);
    Serial.println(" centimeters");

    delay(1000);
  }

  std::sort(samples, samples + SAMPLE_IDX);

  if (SAMPLE_IDX % 2 == 1) {
    return samples[(SAMPLE_IDX / 2) + 1];
  } else {
    return ( samples[(SAMPLE_IDX / 2) + 1] + samples[(SAMPLE_IDX / 2) + 1] ) / 2;
  }
}

void loop() {
  long pulseLen;
  long centimeters;

  pulseLen = get_sonar_val();
  inches = pulseLen / 148;
  centimeters = pulseLen / 58;

  Serial.print("Median distance = ");
  Serial.print(" ");
  Serial.print(centimeters);
  Serial.println(" centimeters");
  delay(5000);
}